جامعه بنها                                                        امتحان الفصل الأول – يناير 2011

كلية العلوم                                                        الفرقة الثانية - شعبة كيمياء وفيزياء

قسم الفيزياء                                                      المادة / كهرومغناطيسية و تيار متردد

تاريخ الامتحان  / 29 / 1 / 2011

نموذج إجابة الكهرومغناطيسية

دكتور / علاء أبوهاشم السيد

3- a) Choose the right answer from the following:                                           [10 marks]     i- When a wire of current I and length L is perpendicular to the magnetic field B. The force acting on the wire is

a) I L B cosθ		b) I A B sinθ 		c) zero			d) I L B

ii- If an electron moves in a circular  orbit of area A giving a current I, the magnetic  moment μ is given by

a) I2 A 			b) I A 			c) I A2			d) I2A2

iii-  The magnetization vector M is weak in materials which are

a) paramagnetic          				b) diamagnetic

c) para and diamagnetic			d) non of the above

iv- The efficiency of a transformer is 40 %. The current and voltage in its primary coil are 2A and 200 V, what is the current in its secondary coil if the voltage in it is 20 V?

a)  2 A            		b) 4 A              	c)  6 A                	d) 8 A

v- In RL circuit ε = 100V, R = 10 Ω and L = 0.005 H what is the current after 5 microsecond from opening the switch.

a) 9.9 A 		b) 99 A 		c) 0.99 A 		d) 99.9 A

b) Put ( √ ) or ( × ) on the front of each statement from the following:         [10 marks]

i- In RL series circuit the energy is not vanished.        ( × )

ii- in the figure below the magnetic force directed to upward    ( × )

iii- I2V2 = I1V1 means the transformer is not ideal.      ( × )

iv- The total magnetic flux on an object located inside a magnetic field must be equal zero

( √ )

v- After a long time from closing the switch the inductor is not affect in the circuit.  ( √ )

…………………………………………………………………………………

4- a)     [10 marks]

M / L =  0.09   kg/m  ,  B = 5.4   T

From the figure we see that the current must pass from

Left to right and this leads to a force FB acting on the

wire directed to upward

FB = I L B sin 90 = I L B

Because the wire is at equilibrium we can write

Mg  =  2 T  +  FB

When the tension in the two strings is zero then

Mg  =  0  +  FB

Mg  =  I L B

I =  Mg / L B  = (M / L) . (g / B)

I = 0.09 × (9.8 / 5.4)  =  0.163 A         so

b) [10 marks]

F/L = 20 N/m ,  a = 0.1 m

Let the location of the line in the

plane of the two wires which the

total magnetic field is zero is at

the point p as in the figure.

The point p is at distance d from

The upper wire and 0.1 – d from

the lower wire.

The force between the two wires is  , where   a = 0.1 m  so

I2 = (2π a F) / (μo I1 L)

I2 = (2 π × 0.1 × 20 ) / (4π × 10 -7 × 10 )

I2 = 106 A

The magnetic field due the upper wire at p is    into the page

The magnetic field due the upper wire at p is    out of the page

When the total magnetic field at p equal zero B1 must equal to B2

B1 = B2

=

d I2 = 0.1 I1 – d I1

d (I2 + I1) = 0.1 I1

d (106 + 10) = 0.1 × 10

d = 9.999 × 10-7 m

……………………………………………………………………………..

والله ولي التوفيق

# Text boxes

d ≈ 1 μ m

p

d

0.1 – d

●

0.1 m

I1 =  10 A

I =  0.163 A

I

T

T

FB

Mg

Bin

×

×

×

×

×

×

×

×

×

×

×

×

×

×

×

–

V

×

Bin

q